MiniSkybot: Kinematics
l: Distance between wheels
r: Wheel's radius
,
: Local frame
MiniSkybot
l=85mm
r=30mm
Y
R
X
R

---
Kinematics Model (I): Local frame

---
Kinematics Model (II): Global frame
: Robot's orientation
%theta
Translating from local to global frame:
vec P_g = Rotz(%theta) vec P_R
Point referred to the
local frame
Point referred to the
global frame
Rotz(%theta)=left ( matrix{cos%theta # -sin%theta # 0 ## sin%theta # cos%theta # 0 ## 0 # 0 # 1} right )
Rotation matrix
(around z axis)

---
Velocities in the local frame
Differential drive mobile robot:
Two wheels that rotate around XR axis
Constraint: no displacement along XR axis
Linear velocity:
It only has a component v along the YR axis.
No component along the XR axis
w
Angular velocity:
Instant local velocity vector:
This vector includes the linear and angular velocities
referred to the local frame
vec v_R = left ( matrix{V ## 0 ## W} right )

---
Velocities in the global frame
left ( matrix{V_x ## V_y ## Wg} right ) = left ( matrix{cos%theta # -sin%theta # 0 ## sin%theta # cos%theta # 0 ## 0 # 0 # 1} right ) left ( matrix{V ## 0 ## W} right )
vec V_g = Rotz(%theta) vec V_R
Local
 velocity
Global
velocity
Vy = Vsin%theta
(1)
Vx = Vcos%theta
Wg = W

---
Local velocity in function of wheel's speed (I)
Linear velocity:
w_1 , w_2
:Wheel's speed (Rad/s)
r: Wheel's radius
vec v = vec v_1 + vec v_2
Contribution of
wheel 1
Contribution of
 wheel 2
w_1 r
v_1
v_2 = 0
l